## Slide 1: SRO Data Lake
ERSAP Data Lake Implementation
Vardan Gyurjyan JLAB EPSCI Group

## Slide 2: SRO Primary Goal
Accept data with minimal loses
  Minimize SRO dead time
  Give more time for backend (services down the stream) to process data
  Stream-strike functionality: similar to signal delay cables during the triggered readout system
Data-Lake as a design choice for the stream-strike functionality
  Temporary in-memory data storage with possible persistency in case of backend dyskinesia
  Centralized storage of unprocessed frames from all streams
  Ideal for ML applications

## Slide 3: ERSAP Data Lake
Low latency, in-memory storage for structured stream-frames
Elastically scalable
Point-in-time persistency of in-memory stream-frames
  Contains stream-frames missed by the back-end
  User defined horizontal scaling threshold
    Tolerable back-end slowness after which
      Persisted data replication on a different node
      ”delayed” parallel processing of data-frames
Pilot implementation based on Redis
  In memory NoSQL database
  Open source
  Large user/support community

## Slide 4: Data Lake Scaling
P
C
C reads and removes the stream-frame
Data-lake grows if C can not keep up with P
Persistent snapshots of the data-lake
Horizontal scaling of the data-lake in case C vertical scaling in not sufficient
Contains stream-frames
not processed by C
Contains stream-frames
not processed by C’
C’
Replication

## Slide 5: CLARA Data Lake Services
Clara data-lake IO services
  Raw frame read/write
  Clara StreamReceiver service
    Frame header parsing
    Frame payload storage, hashed by the frame-time for easy processing
  Clara StreamConsumer service
    Consumes raw frames or farm payloads of multiple streams

## Slide 6: Rapid Prototyping
Stream Source
Software
12
ERSAP
Data Lake
StreamReceiver
12
StreamReceiver
1
-----
Event-rate = 10KHz
Data-rate = 800MByte/sec
Multi-threaded read
Stream Source
Software
1
-----
Lossless data throughput
(in and out data-lake)
9.6 GByte/sec
StreamConsumer
1
StreamConsumer
12
Multi-threaded write
VTP simulated Data Frame
800MByte/sec max frame size per VTP link.
65us window, 8 FADC per 10Gbps link, maximum 1 hit reported per 32ns, 4 bytes per hit:
13 (Header) + (1+65536/32)*8 = 18454 32bit words => 73816bytes

## Slide 7: Screen Shot

## Slide 8: Summary
Developed and benchmarked ERSAP data-lake prototype.
Demonstrated ~10GByte/sec lossless data throughput in and out of the data-lake.
Work in progress
Thank you